Hour ahead demand forecasting
Load profiles for several facilities at 1hr minute intervals.
Task: Improving hour-ahead forecasting accuracy

---
Overview
Example load profile:

---
Baseline model - 1
Baseline_previous:
Predicting the forecast to be the same as the previous hour

---
Baseline model - 2
Baseline_average:
Predicting the forecast to be the same as the previous hour

---
Cross validation
Sequentially trains the model on a growing dataset, forecasting 1 hour ahead over a window at each step.
RMSE between forecasted and actual predictions calculated.
Average RMSE taken a training score.
Train
< Forecast
Train
< Forecast
Train
< Forecast
Train

---
Grid search
Initial analysis of facilities suggests that the timeseries are already stationary with daily and weekly seasonal trends.
**Compromise** Didn’t include weekly seasonal trend due to run time issues. Daily consideration already exhibited an improvement with respect to baseline models and therefore the additional computational requirement for grid searching was not deemed necessary.
For each SARIMA model, grid searched over the following space of parameters:
ARIMA	Seasonal
p = [0,1,2,3]	p = [0,1]
d = [0,1]	d = [0]
q = [1,2,3]	q = [0,1]

---
SARIMA
SARIMA:
Grid searched and cross validated for minimum RMSE on hour ahead forecast

---
SARIMA results so far
Project	Training Baseline – previous RMSE	Training Baseline – average RMSE	Training SARIMA / RSME
6d8c / (3,0,2)-(1,0,1,24)	34.0 kWh	29.6kWh	3.93 kWh
5526 / (1,1,2)-(1,0,0,24)	91.0 kWh	102 kWh	23.8 kWh
1074 / (1,0,2)-(1,0,0,24)	28.1 kWh	26.8 kWh	9.3 kWh
Others still to be tested….